## Slide 1
Problem Statement & Objectives
Intelligent Network Configuration Assistant
01
Intelligent Network
Configuration Assistant
Local automation using MCP on Linux
Problem
Manual network changes are easy to mistype and difficult to audit. Giving an LLM unrestricted shell access adds unnecesary risk.
Objectives
Expose 10 constrained network tools.
Enforce validation and YAML policies.
Verify changes and record audit evidence.
Evaluate reliability and performance in containers.
Notes: Project scope: a local Fedora prototype with a command-line interface. Tools cover IP/port blocking and removal, per-host outgoing bandwidth limits, ping, iperf3 and rule inspection. The model selects a tool; trusted Python code authorizes and executes it. No arbitrary shell execution tool is exposed. Source: project requirements and implementation shared in this conversation.

## Slide 2
Architecture / Mechanism
Intelligent Network Configuration Assistant
02
Example request: “Block TCP port 23”
2 Ollama + Qwen3
Local HTTP, port 11434
1 Terminal client
Linux: chat.py
3 MCP server
Inside admin container
6 Kernel + verification
iptables, tc, ping, iperf3
5 Command runner
Fixed arguments, shell=False
4 Validation + policy
Python services and YAML
Client receives JSON selection and sends MCP via Docker exec stdin/stdout
Audit JSONL and structured result return to the terminal
Lab: admin .10, Client A .20, Client B .30 on 172.30.50.0/24.
Admin controls its own traffic. Direct client-to-client traffic bypasses admin.
Notes: Control messages: chat.py calls ollama_planner.choose_tool over local HTTP, receives schema-constrained JSON, and calls session.call_tool. The client starts src.server through docker compose exec -T admin. MCP uses stdio, not a published server port. FastMCP dispatches constrained wrappers to backend services. Validators reject malformed values; YAML policies reject protected or out-of-range requests. The centralized runner uses a list of fixed arguments with shell=False and captures return code, output and duration. NET_ADMIN allows network changes in the admin namespace. Linux enforces packet rules, not Qwen. Post-operation inspection validates mutations; audit records persist through the /app/logs bind mount. The admin is an endpoint, not a forwarding router. Source: implemented project in this conversation. Official background: https://docs.ollama.com/capabilities/structured-outputs and https://github.com/modelcontextprotocol/python-sdk

## Slide 3
Issues Fixed / Evaluation
Intelligent Network Configuration Assistant
03
Issue | Fix and observed outcome
Unsafe config changes | Validation checks and YAML policy checks
Limited traceiblility | Recorded decisions and execution results
121
unit tests passed
79 / 79
application audit matches
4.74 Mbps
received with a 5 Mbps cap
Improvements:
  Controlled AI execution: Only approved MCP tools can trigger network operations.
  Safer testing: Dry-run mode previews operations before live execution.
  Simplified administration: Natural-language requests reduce dependence on command syntax.
Notes: Evidence shown by the user: 121 pytest tests passed; the final NFR suite found exactly matching final audit records for 79 application request IDs. The first NFR run failed because the running admin container had no logs mount; records stayed inside the container. Recovery and recreation with ../logs:/app/logs:Z fixed persistence. tc class JSON used class instead of kind and flat rate/ceil values of 625000 bytes/s for 5 Mbps; regression tests and a retry corrected verification. iperf3 measured 4.74 Mbps receiver and 4.96 Mbps sender over the limited run. Native Qwen tool calling returned truncated prose; a JSON-schema planner then selected block_port correctly in dry-run. The natural-language live demonstration was instructed, but a full successful live transcript was not supplied. Do not infer a verified natural-language live success from the dry-run result.

## Slide 4
Non-Functional Testing Parameters
Intelligent Network Configuration Assistant
04
Parameter | Method / evidence
Security | Protected port, malformed IP and outside-lab requests rejected.
Reliability | 8 concurrent calls results in 1 change and 7 no-ops.
Auditability | 79 application responses matched their final audit records.
Bounded failure | Unreachable ping returned in 3.10 s against a 12 s test budget.
Capacity | 100-rule limit: tested overflow rejection and capacity after removal.
Live MCP latency, 20 samples per operation
Operation | Median (ms) | P95 (ms)
Repeated block, no change | 7.801 | 8.649
Add block | 11.571 | 12.066
Remove block | 29.423 | 33.438
Notes: Source: user-pasted docs/nfr-results.md, final PASS run dated 8 September 2026. The suite passed 18 checks. Concurrency batch duration was 48.93 ms. Bounded failure duration was 3104.46 ms and the 12000 ms budget is a project test assumption, not an externally approved SLA. Maximum latency: repeated no-change 9.411 ms, add 12.624 ms, removal 34.246 ms. P95 uses nearest rank on 20 samples. Scope includes live MCP dispatch, backend policy, kernel commands and audit, but excludes server startup and LLM inference. Capacity script fills the configured limit, rejects the next addition, verifies removal frees capacity and cleans up. The user said it was done but supplied no capacity result, so no measured capacity PASS is asserted. Schema-level rejections appear in client evidence, not backend audit.

## Slide 5
Challenges Faced
Intelligent Network Configuration Assistant
05
Challenge | Response / remaining limitation
Ambiguous administrator requests | Convert natural language into structured requests and clarify missing details.
Risk of unauthorized network changes | Enforce policies, protect critical services, and restrict available operations.
Integration across multiple technologies | Use MCP interfaces and modular Python components.
Audit persistence and coverage | Maintain structured audit logs for requests, decisions, and outcomes.
Notes: The model latency is one observed request, not a median or benchmark. Qwen3:4b used Ollama on Fedora with about 23 GiB RAM available at the time reported. GPU usage was not established. Preserve the distinction between unit tests, direct MCP integration evidence, and natural-language interaction evidence. The backend has live firewall and bandwidth results, while the supplied model transcript proves JSON selection and dry-run dispatch. Stored pending phases support investigation and retries but do not establish complete crash recovery. The slides use only evidence visible in the conversation and explicitly mark missing evaluation evidence.